2013 Southwest Wisconsin Too hot to Farm Tractor Pulling Rules

All rules must be met upon the first pull of the 2013 pulling year or will not be allowed to participate.

- 3000 RPM Max. RPM pickup required with lead wire installed externally upon the frame of the tractor. Lead wire must be without breaks or connections between pick up and 3 pin connector. 3 pin connector need to be mounted on the rear of the tractor at an easily accessible location.

- 15-18MPH pace. This class will have a pace drawn from a hat by the first puller of the class. All speeds will be used before speeds are returned to the hat. Example – If at the Cuba City pull the first puller draws 16MPH the class will be 16MPH. The next pull the first puller of the class will choose a speed from the hat from 15,17, or 18MPH. If the puller chooses 18MPH the third pull using these rules will allow the first puller of the class to choose from the hat containing the speeds 15 or 17MPH.

  - If the promoting location chooses to have a second too hot to farm class; the promoter may choose to use another speed from the hat or a speed of their choice if any.

- 11,500# will be the weight of the class at all locations

  - If the promoting location chooses to have a second too hot to farm class; and wants a different weight they may choose +/- 500# of the original 11,500# class. Example the second class could be 11,000# or 12,000#.

- Tires will be limited to 20.8R38 or 18.4R42 tires. No cut tires will be allowed

- Intercoolers will be allowed, but only using an OEM manifold and running engine fluids. NO ICE BOXES! Example- if an IH chooses to install an intercooler off a DT bus engine or equivalent that was an IH part number this will be allowed but no aftermarket intercoolers or headers.

- Water injection is allowed using water only. Location and number of nozzles for injection is not restricted

- Must have Steel flywheel OR clutch housing safety blanket

- Must have Kill switch / Air shut off

- Cross bolts mounted in exhaust pipe. 2 - 3/8” grade 8 bolts making a crossing pattern mounted within 1” of each other. The closer to the exhaust wheel of the turbo the better.

- Wheelie bars to be securely mounted to the rear of the tractor

- Only one fuel is permitted.

- Drivers must be at leased 14 years of age with tractor driving certificate and parental consent.

- All other general tractor pulling rules apply