2013 Southwest Wisconsin Farm Tractor Pulling Rules

General Farm Tractor pulling rules

- Rubber tires only. No chains,duals,4x4, or studs Permitted

- All minors must be 14yr of age with written consent from guardian and have tractor driving certificate.

- Tractor must have standard block and crankcase

- Tractors must have original injection pump and if equipped with a blower. It must have factor stock number and no visible modifications.

- All weight must be safely secured to tractor. Any ballast or external part lost while hooked to sled under green flag will result in a disqualification.

- Tractor must have workable rear brakes.

- Tractor must have working PTO and Hydraulics.

- Drawbar is to be stationary in all directions while hooked to sled and pulling. Maximum height of 20 Inches from top of hitching device parallel to ground. Drawbar must have a opening of 3.5 inches and at leased a 6 inch clearance from all weights!

- No one allowed on track except for track officials and contestants.

- Any portion of the tractor going out of bounds will result in a disqualification.

- First puller of the class must use the pull.

- One fuel only is permitted. Tractor must use stock fuel for make and model of tractor. Gasoline, diesel, or propane are considered primary stock fuels. Ether, Oxygen, Alcohol, and various forms of Nitromethane are not allowed!

- All exhaust must be discharged vertically upward with a minimum exhaust height of 12 inches.

Non Turbo Farm Tractor

- 18.4R38 uncut tires or smaller; unless factor equipped with wider tire in which competitor must use be using factor cast wheels.

- 3000 RPM maximum

- Weight at the discretion of the promoter

- 8 MPH or less at the discretion of the promoter.

Turbo Farm Tractor

- 20.8R38 or 18.4R42 uncut tires or smaller; unless factor equipped with wider tire in which competitor must use be using factor cast wheels.

- 3000 RPM maximum

- Weight at the discretion of the promoter

- Non-altered turbos. No slots, Slugs, Billet wheels, or waste gates are allowed.

- 10 MPH or less at the discretion of the promoter.

Hot Stock Tractor

- 18.4R38 cut tires

- Open RPMs w/ safety equipment

- 6000-6500#s will be the weight of the class by discretion of promoter.

- Up Draft Carburetors only

- Gas, Propane, or Diesel Fuel only. No Alcohol

- No turbos

Modified Farm Tractor

- 3000 RPM Max.

- 12 MPH pace.

- 8000 - 9000# will be the weight of the class by discretion of promoter.

- Tires will be limited to 18.4R38 or 20.8R34 tires. No cut tires will be allowed

- Water injection is allowed using water only. Location and number of nozzles for injection is not restricted