Revised 6/15/17

St. Croix Valley Collectors

2017 Pulling Season

Antique Rules

Weights: 2500, 3500, 4500, 5500, 6500 lbs.

- General rules apply.

- Tractors 1957 and older. Grace weight will be 100 lbs in this class

- Speed limits up to 4500 lbs 3 mph. 5500 lbs and up 4 mph. Stock rpm’s will be checked. Not allowed to shift torque or gear while pulling. Engine speed must be controlled by the throttle lever only. No strings or wires allowed.

- Clevis must have a 3 inch hole minimum. Must swing free and not bolted on. (No D Rings)

- Tires can only be one size over factory. No press steel rims unless factory. Steel wheels pull last in there class.

- Rear wheel and/or bolt on frame weights allowed. No hanging suitcase or homemade weight brackets allowed.

- Factory mufflers, No straight pipes allowed unless OEM equipped.

- PTO, Hydraulics and factory air cleaners must be functional on tractors equipped with such devices.

- Maximum drawbar height to be 16 inches, Hitch must be as it came from the factory-unaltered for that specific tractor. Drawbar length minimum of 14 inches from the end of the PTO shaft to the center of the drawbar hole. (Rigid in all directions.)