Revised 6/15/17

St. Croix Valley Collectors

2017 Pulling Season

Classic Rules

4500, 5500 lbs.

5 MPH speed limit, tire size maximum 15.5x38

6500, 7500 lbs.

5 MPH speed limit, tire size maximum 18.4x38

- General rules apply.

- (Horsepower to weight ratio rule applies per Nebraska test.)  4500/45hp, 5500/55hp, 6500/65hp, 7500/75hp.

- Only factory stock engine block and heads allowed. No electric fuel pump. No 800 components in Minneapolis Moline’s. Block, driveline/transmission and sheet metal must be of same manufacturer. No gear reduction starters in Classic, but allowed in Improved.

- Tractors may run up to 10% over farm stock rpm’s. Engine speed must be controlled by stock throttle lever only. No strings or wires allowed.

- Press steel rims allowed. No cut tires. No stripping tractors to make weight class.

- Engine side shields not allowed unless originally equipped OEM. Must be removed for tech inspection if required by the executive committee.

- Must have factory frames and front end. Tractors must have working hydraulics and/or PTO if equipped.

- Suitcase weights and custom made weight brackets are allowed.

- Electronic pickup inside the original distributor housing and stock appearing coils are allowed.

- Hitches can be no more than 20 inches in height.